## Slide 1: Thermomechanical Solver Milestone I
Keith Ballard
Aerospace Engineering

## Slide 2: Unified Design Pros/Cons
Pros
  The temperature function’s gradients for each cell are no longer needed by the elasticity solver, now the gradients can be computed directly from the temperatures at the assembly
  Simplifies output
  Allows two way coupling
Cons
  Makes the assembly more complicated than each solver used to be respectively (easy to overcome)

## Slide 3: Current Design
Executive Class
Thermal Solver
Elasticity Solver
DoF Handler (1)
DoF Handler (dim)
Assemble
Solve
Compute Gradients
Assemble
Solve
Pass Gradients
Output VTK
Output VTK
Combine outputs

## Slide 4: Next Design
Executive Class
DoF Handler (dim + 1)
Assemble Block Matrix
Solve Temperature (Top Left Block)
Solve Elasticity (Bottom Blocks)
Heat Equation Stiffness | Thermal terms from deformation (0)
Displacement terms from thermal strains | Elasticity Equation Stiffness
Temperature
Displacement
Heat Generation
Body Forces
*
=

## Slide 5: Unified Design Pros/Cons
Pros
  The temperature function’s gradients for each cell are no longer needed by the elasticity solver, now the gradients can be computed directly from the temperatures at the assembly
  Simplifies output
  Allows two way coupling
Cons
  Makes the assembly more complicated than each solver used to be respectively (easy to overcome)

## Slide 6: Future Work
Add time dependence
  Modify the heat equation
  Elasticity remains the same (quasi-static)
Parallelize
  Distribute the mesh
  Each process computes stiffness terms for the cells it owns
  Learn how to deal with constraints in deal ii for distributed meshes